## Slide 1: Assembly Basics
Zhen Huang
DePaul University

## Slide 2: Agenda
Intel x86 Processors
Assembly Instruction Syntax
Generic Registers
Example Assembly Instructions
Moving Data
Simple Memory Addressing Mode
Exercise

## Slide 3: Intel x86 Processors
Dominate laptop/desktop/server market
Evolutionary design
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time went on
Model | Release Date | # Transistors | Frequency (MHZ)
8086 | 1978 | 29K | 5-10
80386 (IA32) | 1985 | 275K | 16-33
Pentium 4E (x86-64) | 2004 | 125M | 2800-3800
Core i7 | 2008 | 731M | 1700-3900

## Slide 4: 2015 State of the Art
  Core i7 Broadwell 2015
Desktop Model
  4 cores
  Integrated graphics
  3.3-3.8 GHz
  65W
Server Model
  8 cores
  Integrated I/O
  2-2.6 GHz
  45W

## Slide 5: x86-64
16 generic 64-bit integer registers
  rax, rbx, rcx, …., r8, r9, r10, … r15
Large number of instructions
  Move data: mov
  Compute memory address: lea
  Procedure call: call/ret
  Branching: jmp/jnz/jz/jp/jnp/jo/jno
  Arithmetic/logical operations: add/sub/mul/div/and/or
  Comparison: cmp/test
Various memory addressing modes
  register: (%rbx)
  register+offset: -4(%rbp)
  registerbase+registerindex*scale+offset: 8(%rdx, %rcx, 2)
  constant: 0x400700

## Slide 6: Assembly Instruction Syntax
Linux uses AT&T Assembly Language Syntax
General form of instruction: mnemonic src, dest
  mov %rax, %rbx
  add %rax, %rbx
A mnemonic may include a suffix to specify the size of the operands
  q – quad word 8 bytes, l – long word 4 bytes, w – word 2 bytes, b – byte
  movl $0x11223344,-0x4(%rbp)
Register names starts with %
Immediate data (constant integer) starts with $
  mov $1000, %esi

## Slide 7: x86-64 Integer Registers
%rsp
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 8: Assembly Instruction Example - mov
C Code
Assembly
  %rbx represents dest
  %rax represents t
  %rdi represents s
*dest = t;
s = t;
movq %rax, (%rbx)
mov %rax, %rdi

## Slide 9: Assembly Instruction Example – call/ret
C Code
Assembly
  A procedure name is a label
  A procedure call passes arguments in registers, e.g. %rsi, %rdi
  Return value passed back in %rax
long sub(long x, long y) {
return x – y;
}
int main() {
long t = sub(2000, 1000);
sub:
....
retq
main:
....
mov $0x3e8, %esi
mov $0x7d0, %edi
call sub
mov %rax, -8(%rbp)

## Slide 10: Assembly Instruction Example – arithmetic & logical
C Code
Assembly
  add instruction adds source into dest
  sub instruction subtracts source from dest
long t1 = x + y;
long t2 = t1 >> 3;
long t3 = z - t2;
long t4 = t3 << 3;
long t5 = t4 ^ z;
addq %rsi, %rdi
sarq $3, %rdi
movq %rdx, %rax
subq %rdi, %rax
salq $3, %rax
xorq %rdx, %rax

## Slide 11: Moving Data
Moving Data
  movq Source, Dest:
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “address modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN

## Slide 12: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 13: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 14: Exercise - 1
Explain what’s the effect of each instruction
  mov $10, %rax
  mov $5, %eax
  movl $12345678, (%rbp)
  mov (%rbx), %rcx
  mov %rdi, -4(%rbp)
  add %rcx, %rdx
  salq $2, %rax
  call decode
  ret

## Slide 15: Exercise - 2
What is the value of %rdi after running the instructions?
  mov $1, %rdi
  mov $2, %rsi
  add %rsi, %rdi
What is the value of %eax after running the instructions?
  movl $0x9876, %eax
  sarl $4, %eax

## Slide 16: Exercise - 3
Given the instructions of procedure LSB
  LSB:
  mov %edi, %eax
  and $0xf, %eax
  ret
What is the value of register %esi after running the instructions?
  mov $0xABCD, %edi
  call LSB
  mov %eax, %esi