## Slide 1: Bit Manipulation - 1
Zhen Huang
DePaul University

## Slide 2: Agenda
Bit Positioning
Basic Bit Operations
Bit Mask
Exercise

## Slide 3: Bit Positioning
First bit position (LSB) is designated as position 0.
  Bit positions for a byte: 7 6 5 4 3 2 1 0
  Even-numbered bits: 6 4 2 0
  Odd-numbered bits: 7 5 3 1
Bit 0?
Bit 5?
Bit 7?
Position | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Value | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1

## Slide 4: Basic Bit Operations
Boolean operations
  Bit NOT (complement)(~): 1 -> 0, 0 -> 1
    e.g. ~1011 = 0100
  Bit AND (&)
    1 only when operands are 1
    0 otherwise
  Bit OR (|)
    0 only when operands are 0
    1 otherwise
  Bit XOR (^)
    1 when operands diff
    0 otherwise
A | B | A & B | A ¦ B | A ^ B
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0

## Slide 5: bits-ops.c
Type in the program and run it.
#include <stdio.h>
int main() {
int a, b;
printf(“A B A&B A|B A^B\n”);
for (a = 0; a <= 1; a++)
for (b = 0; b <= 1; b++)
printf(“%d %d %3d %3d %3d\n”, a, b, a&b, a|b, a^b);
}

## Slide 6: Basic Bit Operations - 2
Logical Shift Operations
  Move all of the bits to the left or right
  Left shift (<<)
    value << num_shifts
  Right shift (>>)
    value >> num_shifts
Position | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Value | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
Value << 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
Value >> 1 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1

## Slide 7: Bit Mask
A group of bits used to determine the value of specific bits in another value
Typical usage:
  0s for bits to be ignored
  1s for bits of interest
  Bit AND with the value
e.g. get the values of lowest 2 bits of 0x96 (10010110b)
  bit mask: 0x3 (11b)
  0x96 & 0x3 = 0x2 (10b)

## Slide 8: Bit Mask- Intermediate
Mask the sign bit
  create a mask with 1
  shift the 1 in the mask to MSB
  bit AND with the mask
  int getsignbit(int value) {
  int mask = 1;
  mask = mask << 31;
  return value & mask;
  }
Mask the lowest k bits
  create a mask using (1 << k) – 1
Mask k bits anywhere in the middle
  shift the mask (1<< k) – 1 to the corresponding position

## Slide 9: Bit Mask: examples
Mask the lowest 5 bits
  int mask = (1 << 5) – 1;
  0100000b
  - 1
  ---------
  0011111b
Mask bit position 7 through 4
  int mask = (1 << 4) – 1;
  mask = mask << 4; /* 11110000b */
Mask bit position 5 through 3
  int mask = (1 << 3) – 1;
  mask = mask << 3; /* 00111000b */

## Slide 10: Bit Mask - Advanced
Combining more than one masks
  bit OR (|) individual masks
  E.g. Masking bit position 7 through 5, 3 through 2
  int mask_7_5 = ((1 << 3) – 1) << 5; /* 11100000b */
  int mask_3_2 = 0x3 << 2; /* 00001100b */
  mask = mask_7_5 | mask_3_2; /* 11101100b */
From mask for byte to mask for int
create mask for byte mb
create mask for short ms : (mb << 8) | mb
create mask for int mi: (ms << 16) | ms
  E.g. Masking even-numbered bits, e.g. bit 30, 28, …, 4, 2, 0
  char mb = 0x55; /* 01010101b */
  short ms = (mb << 8) | mb; /* 0x5555 */
  int mi = (ms << 16) | ms; /* 0x55555555 */

## Slide 11: Exercise
Calculate boolean bit operations
  10100101b & 01110011b
  01011100b | 11010001b
  11000011b ^ 01101100b
Create bit masks
  Bit position 2, 1, 0
  Bit position 6,4,3
  Bit position 7,3,2,0