## Slide 1: Control Program Execution - 1
Zhen Huang
DePaul University

## Slide 2: Agenda
Jump Instruction
Condition Codes
Conditional Jump Instructions
Exercise

## Slide 3: Jump Instruction
A jump instruction changes the address of the next instruction to execute
JMP dest
  Update Program Counter (PC) with the destination address
  jmp .L1: e.g. jmp 0x40054c
  jmp *%rax : destination address via rax
  jmp *(%rax) : destination address via pointer rax
Equivalent to goto statement in C
  goto abort:
  ….
  abort:
  return -1;

## Slide 4: Jump Instruction - Example
Address | Content
0x400540 | 0x10
0x400541 | 0x06
0x400542 | 0x40
0x400543 | 0x00
0x400544 | 0x00
0x400545 | 0x00
0x400546 | 0x00
0x400547 | 0x00
Instruction | PC afterwards
jmp 0x40052d | 0x40052d
jmp *%rbx | 0x40037f
jmp *(%rax) | 0x400610
Register | Value
%rax | 0x400540
%rbx | 0x40037f

## Slide 5: Condition Codes (Implicit Setting)
Carnegie Mellon
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (think of it as side effect) by arithmetic operations
  Example: addq Src,Dest ↔ t = a+b
  CF set if carry out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by leaq instruction

## Slide 6: Condition Codes (Explicit Setting: Compare)
Carnegie Mellon
Explicit Setting by Compare Instruction
  cmpq Src2, Src1
  cmpq b,a like computing a-b without setting destination
  CF set if carry out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)

## Slide 7: Condition Codes (Explicit Setting: Test)
Carnegie Mellon
Explicit Setting by Test instruction
  testq Src2, Src1
    testq b,a like computing a&b without setting destination
  Sets condition codes based on value of Src1 & Src2
  Useful to have one of the operands be a mask
  ZF set when a&b == 0
  SF set when a&b < 0

## Slide 8: Reading Condition Codes
Carnegie Mellon
SetX Instructions
  Set low-order byte of destination to 0 or 1 based on combinations of condition codes
  Does not alter remaining 7 bytes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 9: x86-64 Integer Registers
%rsp
%al
%bl
%cl
%dl
%sil
%dil
%spl
%bpl
%r8b
%r9b
%r10b
%r11b
%r12b
%r13b
%r14b
%r15b
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 10: Reading Condition Codes (Cont.)
cmpq %rsi, %rdi # Compare x:y
  setg %al # Set when >
  movzbl %al, %eax # Zero rest of %rax
ret
Carnegie Mellon
SetX Instructions:
  Set single byte based on combination of condition codes
One of addressable byte registers
  Does not alter remaining bytes
  Typically use movzbl to zero-extend to other bytes
    set upper bits to 0
int gt (long x, long y)
{
return x > y;
}
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value

## Slide 11: Conditional Jump Instructions
Carnegie Mellon
jX Instructions: jump only when certain condition is satisfied
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 12: Conditional Jump Example - 1
absdiff:
cmpq %rsi, %rdi # x <= y?
jle .L2 # yes
movq %rdi, %rax
subq %rsi, %rax
ret
.L2: # x <= y
movq %rsi, %rax
subq %rdi, %rax
ret
Compiled using “gcc –Og –S control.c”
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rax | Return value
long absdiff
(long x, long y)
{
long result;
if (x > y)
result = x-y;
else
result = y-x;
return result;
}

## Slide 13: Conditional Jump Example - 2
int sum(int n) {
int sum = 0;
while (n > 0) {
sum += n;
n--;
}
return sum;
}
sum:
movl $0, %eax # sum = 0
jmp .L2
.L3:
addl %edi, %eax # sum += n
subl $1, %edi # n--
.L2:
testl %edi, %edi # n > 0?
jg .L3 #
rep ret
Compiled using “gcc –Og –S sum.c”

## Slide 14: Exercise
Save the following C code into cond.c and compile it into assembly code using
“gcc –Og –c cond.c”
int max(int a, int b) {
if (a > b)
return a;
else
return b;
}
int min(int a, int b) {
if (a < b)
return a;
else
return b;
}
Q1. What jump instruction is
used in max?
Q2. What jump instruction is
used in min?
Q3. What’s the difference
between the assembly
instructions of max and min?

## Slide 15: Exercise - Continued
Copy /home/zhuang/public/jumps.s to your home directory
Read jumps.s and figure out what will it print when it is executed
Check your result by compiling and running the code:
    gcc –o jumps jumps.s
    ./jumps